## Slide 1: Machine-Learning-Enabled Design for Molten Salt Reactors
Nuclear, Plasma and Radiological Engineering, University of Illinois at Urbana-Champaign
Big Data for NPPs Workshop, The Ohio State University Columbus, OH - Dec. 10-11, 2019
Mehmet Turkmen, Kathryn D. Huff

## Slide 2: Motivation/Aim for This Study
To determine an optimized core design of for Molten Salt Reactors.
To use a novel, robust, reliable, and accelerated method in the designing process.
To make the reactor more efficient, compact, and safe
Aim: To introduce an efficient, robust, and reliable design recommendation approach based on machine learning methods
This talk presents preliminary results using AI/ML to find the optimized reactor parameters rather than traditional optimization methods such genetic algorithms.

## Slide 3: Programs/Codes Used
Criticality calculations: Serpent 2 – Version 2.1.36
  Computational standard deviation of pcm
Neutron data library: ENDF/B-VII.0
  Serpent is not capable of using state-of-the-art ENDF libraries
Programming: Python 3.7
Sampling/Training: Raven Framework (INL)
  Stable version (Nov 19) (https://raven.inl.gov/SitePages/Code.aspx)

## Slide 4: Methods Used
Reactor model: Monte Carlo Technique (Serpent 2)
Target reactor design: Molten Salt Reactor
Sampling methods: Grid Sampling Approach
Training methods: ROMs
  sci-kit learn
    Neural Network
    Decision Tree
    K-Nearest Neighbors
Classification: Data Mining
  Ensemble
  Cluster
Method validation: single fuel channel with unit cell approximation

## Slide 5: Method Validation
Single fuel channel using unit cell approximation
For square lattice cell geometry, 8 independent variables are under investigation for optimization.
Features:
  Fuel type
  Salt type, density and flow rate
  Enrichment (ε)
  Pitch (p) and channel radius (Rf)
  Moderator to fuel ratio
  Channel length
  qchannel (or in terms of Tin and Tout)
Pitch (p)
Moderator
Fuel Salt
Rf
vsalt
Tin
Length (L)
Tout
qchannel

## Slide 6: Input/Target Parameters Selected
Inputs:
  Fuel types: U, U-Th, U-Pu
    - Th as Th-232
    - Pu as weapons-grade Pu
  Salt types: LiF-BeF2, NaF-BeF2, NaCl
    (i) LiF+BeF2 (72/16 mole %)+HM (12 mole %) - MSFR/Mosart/Flibe
    rho(T)=3.628-6.6e-4*T(oC)1 for U-Th
    (ii) NaF+BeF2 (76/12 mole %)+HM (12 mole %) - ThorCon
    rho(T)=5.52-1.964e-3*T(oC)2 for U
    (iii)NaCl (60 mole %)+HM (40 mole %) - Terrapower/Elysium/Moltex
    rho(T)=4.29-1.59e-3*T(oC)2 for U
1 Ref. Jerden, J., 2019. Molten Salt Thermophysical Properties Database Development: 2019 Update. Chemical and Fuel Cycle Technologies Division, ANL/CFCT-19/6
2 Ref. Janz, G.J., 1988. Thermodynamic and Transport Properties for Molten Salts: Correlation Equations for Critically Evaluated Density, Surface Tension, Electrical Conductance, and Viscosity Data. ThermoJournal of Physical and Chemical Reference Data 17 (2) 1–309.

## Slide 7: Input/Target Parameters Selected
Inputs:
  235U fissile content (ε): 1 to 20 wt. % in HM
  U content: 10 to 90 wt. % in HM
    - 100 wt. % for U type
  Pitch (p): 1 to 16 cm
    - based on MSRE design
  Vmoder/Vsalt: 0.274 to 10.46
    - minimum value: 0.274 for p=Df
    - maximum value: 10.46 for p=3Df
  Tfuel-average: 900 to 1200 K
Outputs:
  Infinite multiplication factor ()
  Conversion ratio (CR)
  Fast flux on moderator
  Total feedback coefficient (αD+αV+...)

## Slide 8: Assumptions/Approximations/Simplifications
Tfuel-aver instead of q'channel over a fuel channel length of 1m
Only neutronic calculations are under consideration
  Thermal-hydraulics effects are ignored
  Stationary fuel salt
Base-line temperature 900 K for feedback calculations
  Temperature is the main driver for fuel salt density and Doppler feedback
Calculations just for initial fuel loading

## Slide 9: Computational Flowchart
Raven Framework
Samplers
Grid method
Distribution
Reduced Order Models
(Regressors)
External Physical
Model
Code Interface + Serpent2
Input:
Fuel, Salt, 235U wt%, U wt%, p, Tfuel-ave, Vmoder/Vsalt
Data Structures
Runs
Sampling
Training
Output:
k∞, CR,
φfast(graph), αfeedback
SciKitLearn etc.
Post-processing
HDF5, Print, Plot,...
Data Mining
(Clustering)
Agglomerative, K-Means etc.

## Slide 10: Grid Sampling Approach
The simplest exploration approach to explore an uncertain domain
Construct an N-dimensional grid where each dimension is represented by one uncertain variable
Equal distances
Performs the sampling at each node of the grid
Total number of samples: 31500
Variable | Fuel Type | Salt Type | 235U Content | U content | Pitch | Vmoder/Vsalt | Tfuel-average
Distribution | Discrete | Discrete | Continuous | Continuous | Continuous | Continuous | Continuous
Lower/Upper Values | U, U-Th, U-Pu | LiF-BeF2, NaF-BeF2, NaCl | 1-20 wt.% | 10-90 wt.% | 1-16 cm | 0.274-10.46 | 900-1200
Step Sizes | 3 | 3 | 7 | 5 | 5 | 5 | 4

## Slide 11: Data Mining
Options | KMeans | AgglomerativeClustering | DBScan
Classification | cluster | cluster | cluster
Solver | k-means++ | ward | eps=0.2
# of Clusters | 8 | 8 | min_samples=20
Metric |  | euclidean | euclidean
Search for how the targets are to be clustered
Identify the decision boundaries and classes
Training data: Inputs (fuel type, ...) + Outputs (, ...)
Those methods do not necessarily require target(s)
Rest of the options are set to the default value

## Slide 12: Reduced Order Methods
Methods | Class | Options
RandomForestRegressor | Ensemble | n_estimators=200
DecisionTreeRegressor | Decision Tree | -
KNeighborsRegressor | Neighbor Based | n_neighbors=20
MLPRegressor | Neural Network | max_iter=2000
To predict the target values
Training data: Inputs (fuel type, ...)
Target values: Outputs (, ...)
Rest of the options are set to the default value
Some regressors such as AdaBoost Regressor are incapable of training our datasets as they do not support multi-output feature

## Slide 13: Results: Raw Data Distribution

## Slide 14: Results: Regressors
Random Forest and Decision Tree predictions (orange) agree well with the real values (blue)
Neural Network and K-Nearest Neighbors need improvement
kinf
kinf
conv_ratio
conv_ratio

## Slide 15: Results: Regressors
Fast flux per source
Fast flux per source
Feedback coef. (pcm)
Feedback coef. (pcm)

## Slide 16: Results: Regressors
Random Forest and Decision Tree successfully predicted the target values of the test datasets. They have very high score (1) and root mean square (~0) values.
K-Nearest Neighbors and Neural Network totally fail in training the datasets provided.
Neural Network yields completely different results.
Neural Network is highly sensitive to its parameters. They need to be adjusted carefully according to the problem’s nature.

## Slide 17: Results: Clusters- Optimal Cluster Size
Silhouette score and sum of squared distance calculation for cluster size determination
For clustering, optimum cluster size is 3-5. Set to 5 in calculations
KMeans & Agglomerative
Kmeans

## Slide 18: Results: Clusters
conv_ratio
Fast flux per source
Feedback coef. (pcm)
kinf

## Slide 19: Results: Clusters
Decision boundaries are not sufficiently clear
DBScan totally fails in clustering the datasets
Combine clustering method with regression method
Make cluster, select some classes and finally train the data over the selected classes (as a future work)

## Slide 20: Conclusion
Based on the results of regression analyses, the suggested method gives promising results
The results show that the method works well for the fuel channel
It is possible to use this method to predict any target without running reactors physics code
Selection of the right regressors and classifiers is important
Categorical distribution in feature and multi-output in the target limit the use of different methods of Regressors and also Classifiers
Some cluster methods like DBScan do not resolve the search space
The database used in the optimization seems insufficient as the target space is not well-distributed, needs more data for better prediction
Some classification methods require class labels
  Create some labels like ‘fast’ or ‘thermal’ reactor, ‘breeder’ or ‘burner’ (as a future work)

## Slide 21: Future Works
Examine other regressors, clusters and classifiers
Use Monte Carlo based sampler
Expand the suggested method to fuel assembly and then to full-core
Couple to a thermal-hydraulics code (i.e. Moltres)
Perform analyses for equilibrium cycle with reprocessing option
Generate temperature-dependent ENDF/B-VIII.0 ACE libs for Serpent with NJOY21
Burnup and depletion analysis
Uncertainty analysis

## Slide 22: Acknowledgements
This research is part of the Blue Waters sustained-petascale computing project, which is supported by the National Science Foundation (awards OCI-0725070 and ACI-1238993) and the state of Illinois. Blue Waters is a joint effort of the University of Illinois at Urbana-Champaign and its National Center for Supercomputing Applications.
The authors would also like to acknowledge financial support from the Scientific and Technological Research Council of Turkey (TUBITAK) BIDEB-2219 Postdoctoral Research Program.
Prof. Huff is supported by the Nuclear Regulatory Commission Faculty Development Program, the Blue Waters sustained-petascale computing project supported by the National Science Foundation (awards OCI-0725070 and ACI-1238993) and the state of Illinois, the NNSA Office of Defense Nuclear Nonproliferation R&D through the Consortium for Verification Technologies and the Consortium for Nonproliferation Enabling Capabilities (awards DE-NA0002576 and DE-NA0002534), the DOE ARPA-E MEITNER Program (award DE-AR0000983), and the International Institute for Carbon Neutral Energy Research (WPI-I2CNER), sponsored by the Japanese Ministry of Education, Culture, Sports, Science and Technology.

## Slide 23: Thank you for your attention